## Slide 1: Billion Object Apparatus
Concept: optical/IR spectrograph on a 10m telescope
  massively multiplexed (50k-100k fiber)
  wide-field (1-5 deg2)
Primary Objective: complete sampling of linear density field using between 500M and 1B spectroscopic tracers
  Maximal precision on cosmological constraints with clustering to z<3.5
Feasibility: shares instrument design with existing/proposed experiments
  Design for 10-m class telescope with large FOV (Pasquini et al., 2016)
  Spectrograph design for DESI adaptable to 4th infrared channel (1-1.4 micron)
  Tests of target selection and spectroscopic completeness with PFS
Programmatics: Staged development with other spectroscopic surveys
  Similar spectrograph design to DESI, DESI-II
  Shared platform with SSSI
Partnership with DOE labs: R&D to meet technical challenges
  Dense packing of fibers in focal plane
  Scale spectrograph production to 100,000 fibers
  Development of Ge CCDs at LBNL